# Programming Target MCU
1. Connect ICSP+TID to Target board
2. Connect Power supply to Programmer
3. Reset Arduino board
4. Wait till RDY lights up
5. If AUTO is not lit, select Manual program name using DIP switches. Manual program name is something like A1C3, A2D4, etc
6. Press UPLOAD button => OK led will blink 3 times acknowledging that Upload has started
7. Now RDY will blink showing that Programmer is busy
8. Wait till OK is constantly lit acknowledging that programming finished successfully
9. If ERR is lit, then decipher ERR by counting how many times it blinks. See Appendix A.
# Downloading MCU flash to SD
1. Connect ICSP+TID to Target board
2. Connect Power supply to Programmer
3. Reset Arduino board
4. Wait till RDY lights up
5. Press BACKUP button => OK led will blink once acknowledging that Backup has started
6. Now RDY will blink showing that Programmer is busy
7. Wait till OK is constantly lit acknowledging that backup has finished successfully
8. If ERR is lit, then decipher ERR by counting how many times it blinks. See Appendix A.
# Appendix A
Number of error is displayed via ERR led by blinking it for a number of times:
1. No Target device discovered => make sure ICSP is properly connected
2. SD Card failure => Make sure SD Card is attached, properly formatted and proper files are uploaded
3. Auto Program Identification Failed => Make sure Target board is ICSP+TID compatible, and wires are not too long (no noise on wires)
4. No program file found => Make sure file is available on SD Card & Configuration file is updated with TargetID
5. Wrong Target MCU model => Make sure Conf/Program file is correct and Target MCU resembles expected MCU model
6. Corrupted Program file => Fix it or upload new
7. VERIFY: Program file & Target MCU didn't match => See AUTO for details (press and hold BACKUP button)
8. Target MCU communication failure => Make sure cable is not too long, etc
9. no such error
10. General System Failure => See AUTO for mode details (press and hold BACKUP button)
# Appendix B
In order to define more detail error, press and hold BACKUP button to see secondary error code, which will be displayed by RDY led: